Solution 1 for module Thermofluid Dynamics (Aero) 55-504111 Dr Torsten Schenkel Associate Professor of Continuum Mechanics Department of Engineering and Mathematics Sheffield Hallam University Sheffield S1 1WB Tel: +44 (0)114 225 6294 Email: t.schenkel@shu.ac.uk Indicative solutions only. May contain errors. Questions: 1. Consider the flow through a rocket nozzle.

Assume that the gas flow is an isentropic expansion of a calorically perfect gas. In the combustion chamber, the gas which results from the combustion of rocket fuel and oxidiser (Methane/LOX) has a pressure of 15atm and a temperature of 2500K. The molecular weight and specific heat (constant pressure) for the combusted gas is 27 and 2112 J/kgK, respectively1. a. The pressure at the exit (ambient pressure) is 0.372atm.

What is the temperature at the exit? Calculate T from isentropic relations:
𝑇𝑒 𝑇0 = ( 𝑝𝑒 𝑝0 ) 𝛾−1 𝛾 𝑇𝑒 = 𝑇0 ( 𝑝𝑒 𝑝0 ) 𝛾−1 𝛾 𝛾 can be calculated from the thermodynamic properties given: 𝛾 = 𝑐𝑝 𝑐𝑣 where 𝑅𝑠𝑝𝑒𝑐 = 𝑐𝑝 − 𝑐𝑣 𝑐𝑣 = 𝑐𝑝 − 𝑅𝑠𝑝𝑒𝑐 and 𝑅𝑠𝑝𝑒𝑐 = 𝑅𝑔𝑒𝑛 𝑀 = 8314 𝐽 𝑘𝑚𝑜𝑙 𝐾 27 𝑘𝑔 𝑘𝑚𝑜𝑙 = 307.9 𝐽 𝑘𝑔 𝐾 𝛾 = 𝑐𝑝 𝑐𝑝 − 𝑅𝑠𝑝𝑒𝑐 = 2112 2112 − 307.9 = 1.17 so 𝑇𝑒 = 𝑇0 ( 𝑝𝑒 𝑝0 ) 𝛾−1 𝛾 = 2500𝐾 ( 0.372 15 ) 1.17−1 1.17 = 1458 𝐾 b.

Calculate the Mach number and speed at the exit of the engine. Mach number can be calculated from pressure or temperature ratio. From pressure ratio: 1 Can you work these out from the stoichiometry of the combustion?

𝑝 𝑝0 = 1 (1 + 𝛾 − 1 2 𝑀2) 𝛾 𝛾−1 𝑝0 𝑝𝑒 = (1 + 𝛾 − 1 2 𝑀𝑒 2) 𝛾 𝛾−1 ( 𝑝0 𝑝𝑒 ) 𝛾−1 𝛾 = 1 + 𝛾 − 1 2 𝑀𝑒 2 𝑀𝑒 = √ 2 ( 𝑝0 𝑝𝑒 ) 𝛾−1 𝛾 − 1 𝛾 − 1 = 2.9 Speed: 𝑢 = 𝑀 √𝛾𝑅𝑇 = 2097.6 𝑚 𝑠 c.

If the required thrust at that altitude is 4.5 ∙ 105𝑁, what is the mass flow rate through the engine? Thrust of a rocket engine: 𝐹𝑡 = 𝑚̇ 𝑢 𝑚̇ = 𝐹𝑡 𝑢 = 215 𝑘𝑔 𝑠 d. What is the required area (and diameter) at the throat and at the exit to achieve the desired flow?

From mass flow rate at the throat:
𝑚̇ = 𝑢 ∗𝜌 ∗𝐴 ∗ = 𝑎 ∗𝜌 ∗𝐴 ∗ 𝐴 ∗ = 𝑚̇ 𝑎 ∗𝜌 ∗ with: 𝑎 ∗ = √𝛾𝑅𝑇 ∗ = √𝛾𝑅 𝑇0 2 𝛾 + 1 = 911.1 𝑚/𝑠 𝜌 ∗ = 𝜌0 ( 2 𝛾 + 1 ) 1 𝛾−1 ρ0 = 𝑝0 𝑅 𝑇0 = 1.975 𝑘𝑔/𝑚3 ρ ∗ = 1.222 𝑘𝑔/𝑚3

Be aware that you need the pressure in Pa, not atm!
𝐴 ∗ = 𝑚̇ √𝛾𝑅 𝑇0 2 𝛾 + 1 𝜌0 ( 2 𝛾 + 1 ) 1 𝛾−1 = 0.1931 𝑚2 𝑅 ∗ = √ 𝐴∗ 𝜋 = 0.2479 𝑚 ( 𝐴 𝐴∗ ) 2 = 1 𝑀2 [ 2 𝛾 + 1 (1 + 𝛾 − 1 2 𝑀2)] 𝛾+1 𝛾−1 𝐴𝑒 = 𝐴 ∗ √ 1 𝑀𝑒 2 [ 2 𝛾 + 1 (1 + 𝛾 − 1 2 𝑀𝑒 2)] 𝛾+1 𝛾−1 = 1.236 𝑚2 𝑅0 = √ 𝐴0 𝜋 = 0.627 𝑚 2.
A blunt nosed cruise missile is flying at Mach 2 at standard sea level. Calculate the pressure and temperature at the nose of the missile. Easy way: The stagnation point temperature does not change over the shock.
So the stagnation temperature is the same as 𝑇0! 𝑇 𝑇0 = 1 1 + 𝛾 − 1 2 𝑀2 𝑇0 = 𝑇 (1 + 𝛾 − 1 2 𝑀2) = 288𝐾 (1 + 1.4 − 1 2 2 2) = 518.4 𝐾 3. Consider a point in a supersonic flow where the static pressure is 0.4bar. When a Pitot tube is inserted in the flow at this point, the pressure recorded is 3bar. Calculate the Mach number of the flow at that point. TBD